## Slide 1: Chapter 3 Computer Networks: The OSI Networking Model
Dr. Omayma Younis
BIS 416E – Networks & Security

## Slide 2
Learning Objectives
Determine the purpose of the OSI Networking Model.
Identify the seven layers of the OSI model, in order.
Understand how data travels through the OSI layers.
Relate each layer to its corresponding functions, services, protocols, and hardware.

## Slide 3
Introduction
A network communication system is a complex system composed of two main subsystems: hardware and software.
The hardware subsystem identifies how network nodes are physically connected (explained in chapter 2).
The software subsystem identifies how network nodes are logically connected.
Early attempts implemented the software subsystem as a single, complex, unstructured program (i.e. one huge piece of code normally written in assembly language).
Oops! … this resulting software was difficult to test and very difficult to modify.

## Slide 4
Introduction
To overcome this problem, the International Standards Organization (ISO) developed a theoretical model (framework) called the Open Systems Interconnection (OSI) model.
The OSI model adopted a layered-approach in which the complete communication system (software/hardware) is represented through a number of distinct layers, each of which performs a well-defined function.
This “theoretical/conceptual” OSI model was used as a reference for the “real-world” networking systems such as the standard Internet model: TCP/IP model.

## Slide 5
The OSI Reference Model
The OSI model breaks the networking system down into seven layers:
Each layer is responsible for certain functions within the process of sending/receiving data between source/destination.
Each layer is responsible for communicating only with the layers immediately above it and below it.
For instance, the physical layer will never deal directly with the network layer.
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Layer 1
Layer 2
Layer 3
Layer 4
Layer 5
Layer 6
Layer 7

## Slide 6
Overview of the OSI Model
7. Application Layer
6. Presentation Layer
5. Session Layer
4. Transport Layer
3. Network Layer
2. Data Link Layer
1. Physical Layer
The Upper Layers
Define how the applications within the end stations will communicate with each other and with the users.
The Bottom Layers
Define how data is transmitted end to end.
None of the upper layers knows anything about networking or network addresses. That’s the responsibility of the bottom layers.
These bottom layers define how data is transferred through physical media, switches, routers, etc.

## Slide 7
Basic Functions of OSI Layers
7. Application Layer
6. Presentation Layer
5. Session Layer
4. Transport Layer
3. Network Layer
2. Data Link Layer
1. Physical Layer
Provides the user interface, and software applications
Performs data formatting, encryption, and compression
Creates, maintains, and closes sessions.
Breaks data into segments, Ensures successful delivery
Determines the network route via logical addressing
Provides access to media via physical addressing
Places signal on the transmission medium

## Slide 8
Do you remember this?
In chapter 2, the connectivity devices were classified as follows:
Layer-1 Devices
Repeaters
Layer-2 Devices
Bridges
Hubs
Layer-3 Devices
Routers
Switches
This means that Layer-1 devices operate and work within the physical layer only.
Layer-2 devices operate in the data link layer as well, as they use physical addressing (MAC addresses) to determine the destined node.
Layer-3 devices work in the network layer, as they use logical addressing (IP addresses) to determine the network route.

## Slide 9
How data travels within OSI layers
7 : Application Layer
6 : Presentation Layer
5 : Session Layer
4 : Transport Layer
3 : Network Layer
2 : Data Link Layer
1 : Physical Layer
data
data
AH
data
PH
data
SH
data
TH
data
NH
data
DH
DT
data
01000 …. 0011101
data
data
DH
DT
data
NH
data
TH
data
SH
data
PH
data
AH
Sender
Receiver

## Slide 10
How data travels within OSI layers
7 : Application Layer
6 : Presentation Layer
5 : Session Layer
4 : Transport Layer
3 : Network Layer
2 : Data Link Layer
1 : Physical Layer
Receiver
1. The application, presentation, and session layers, takes user input and converts it into ready-data
2. This layer adds a transport header and breaks the data into segments
Sender
3. This layer adds a network header, and converts the segments into packets
4. This layer adds a datalink header & trailer, converting packets into frames
5. Frames are converted into bits, which are placed on the transmission medium
Reverse process
Reverse process
Reverse process
Reverse process
Reverse process

## Slide 11
How data travels within OSI layers
These steps, originating from the sender (source), are known as data encapsulation.
Each OSI layer appends a header (containing layer-specific additional data) and encapsulates them all together.
When the bits stream arrives at the receiver (destination), the whole process is reversed.
First, the physical layer converts the received bits into frames.
Each OSI layer removes its corresponding header, while the data flows up the OSI model until it is converted back into the original data and presented to the receiver. This process is also known as de-encapsulation.

## Slide 12
The Seven Layers of the OSI Model
Let’s have a deeper look at each of the seven layers

## Slide 13
Application Layer (layer-7)
It is the top most i.e. seventh layer of OSI Model. Thereby, it does not provide services to any other overlying layer.
It provides the user interface and enables the user to access the network through a set of software applications (web browser, e-mail client, file transfer application, etc.)
Q: Do applications such as “photoshop” and “notepad” reside at this layer?
A: No, because they do not enable users to access the network. In other words, they are non-communicating applications.

## Slide 14
Application Layer (layer-7)
Functions provided by the Application Layer:
E-mail Services: This application provides various e-mail services. Protocol: SMTP (Simple Mail Transfer Protocol)
Accessing the World Wide Web: Most common application today is the access of the World Wide Web through web browsers. Protocol: HTTP (Hypertext Transfer Protocol) e.g. http://aliallam.net/
File transfer & Access: It allows users to transfer files from/to a remote host. Protocol: FTP (File Transfer Protocol) e.g. ftp://193.43.36.131/Radio/MP3/
Remote log-in: A user can log into a remote computer and access the resources of that computer. Protocol: TELNET

## Slide 15
Presentation Layer (layer-6)
Presentation layer is the sixth layer of OSI Model.
It is concerned with the presentation of the data exchanged between two devices.
On the source-side, it is concerned with data encoding, encryption, and compression.
On the destination-side, it performs data decoding, decryption, and decompression.

## Slide 16
Presentation Layer (layer-6)
Functions provided by the Presentation Layer:
Data Encoding/Decoding (translation): As different computers use different encoding systems, it may convert an EBCDIC-coded text file to an ASCII-coded file. Standards: e.g. ASCII, Unicode, EBCDIC.
Data Encryption/Decryption: it hides the original data by ciphering it. When the encrypted data reaches the destination, it decrypts the message. Protocols: Secure Socket Layer (SSL)
Data Compression/Decompression: it shrinks large amount of data into smaller pieces (i.e. it reduces the size of multimedia data). Standards: e.g. JPEG (for images), MPEG (for videos), MIDI (for sound), etc.

## Slide 17
Session Layer (layer-5)
Session layer is the fifth layer of OSI Model.
It has the responsibility of beginning, maintaining and ending the connection between two devices, called session.
It also provides for orderly communication between devices by regulating the flow of data (e.g. what is the amount of data).

## Slide 18
Session Layer (layer-5)
Functions provided by the Session Layer:
Establishing, Maintaining and Ending a session: When the sender first contacts with the receiver, it sends SYN (synchronization) message to establish a connection and determines the order in which information will be sent. Receiver sends ACK (acknowledgement). So, the session can be established & closed.
Dialog Control: This function determines which device will communicate first and the amount of data that will be sent.
Dialog Separation: Process of adding checkpoints & markers to the stream of data is called dialog separation.

## Slide 19
Transport Layer (layer-4)
At the source side, the transport layer receives the upper-layer data and breaks it into a group of segments (chunks/pieces), and adds a header to each segment.
The transport header contains data such as the sequential number, size of segment, etc.
At the receiver side, it reassembles these segments again onto a single message to be passed to the upper-layers at the destination.
It is responsible for process-to-process delivery of the entire message (i.e. responsible for what is delivered, not where it is delivered).
The underlying layers are responsible of determining the “Where”.

## Slide 20
Transport Layer (layer-4)
Transport Layer provides two types of services:
Connection-Oriented Transmission: In this type of transmission, the receiving device sends an acknowledgement back to the source after a segment or a group of segments is received. It is a slower transmission method, but a more reliable one. Protocol: Transmission Control Protocol (TCP)
Connectionless Transmission: In this type of transmission the receiving device does not send an acknowledgement back to the source. It is a faster transmission method, but less reliable. Protocol: User Datagram Protocol (UDP)

## Slide 21
Transport Layer (layer-4)
Functions provided by the Transport Layer:
Segmentation (partitioning) of the message into segments (at source side), and reassembly of segments onto the message (at destination).
Port addressing: Computers run several processes. The header of this layer includes a port address specifying the process carried out. For instance, port 23 is reserved for Telnet services, and HTTP uses port 80 for providing web browsing service, and 21 for FTP, etc.
Flow Control: it prevents the source form sending data packets faster than the destination can handle.
Error Control: it ensures that the entire message arrives at the receiving transport layer without any error.

## Slide 22
Network Layer (layer-3)
It converts the segments into packets by adding the network header (NH), which contains information about the network address of source and destination.
It is responsible for the source-to-destination delivery of a packet across multiple networks.
If two systems are attached to different networks with devices like routers, then this means that the network layer is used.
Routers (layer-3 devices), which work within the network layer, determine the network route via logical addressing (IP addresses).
It also determines alternative routes from source-to-destination, and calculates the route distance.

## Slide 23
Network Layer (layer-3)
Functions provided by the Network Layer:
Internetworking: It provides communication between different networks.
Logical Addressing: When a packet is sent outside the network, the network layer adds logical (network) address of the sender & receiver to each packet. Protocols: Internet Protocol (IP), IPX
Network addresses are assigned to local devices by network administrators, and obtained dynamically by the DHCP (Dynamic Host Configuration Protocol)
Routing: When independent networks are connected to create an internetwork, several routes are available to send the data from source to destination. These networks are interconnected by routers that route the packet to its final destination.

## Slide 24
Data Link Layer (layer-2)
It is responsible for node-to-node (end-to-end) delivery of data.
It receives the packet from the network layer and creates frames, by adding a datalink header (DH) containing the physical addresses (MAC Address), and passes them to the physical layer.
It also appends a datalink trailer which contains information used for error detection, such as cyclic redundancy check (CRC).
As mentioned before, switches and bridges operate within layer-2.
It consist of two sublayers:
  Logical Link Layer (LLC)
  Medium Access Control (MAC)

## Slide 25
Data Link Layer (layer-2)
  Logical Link Layer (LLC) : responsible for identifying network-layer protocols, and then encapsulating them.
  Medium Access Control (MAC): responsible for identifying how frames are placed on the media (first come/first served). A MAC header defines the physical address of source and destination. It is also responsible for error detection/notification (but not correction).
Data Link Layer
Logical Link Layer (LLC)
Medium Access Control (MAC)

## Slide 26
Data Link Layer (layer-2)
Functions provided by the Data Link Layer:
Framing and Physical Addressing: it converts packets received from network layer into frames, by adding the physical addresses of the sender and receiver (MAC address) in the header of each frame.
Overflow Detection: it prevents the fast sender from drowning the slow receiver.
Error Detection: It provides the mechanism of error control in which it detects damaged or lost frames.
Access Control: When single communication channel is shared by multiple devices, the MAC sublayer determines which device has access over the channel (first come/first served).

## Slide 27
Physical Layer (layer-1)
It is the bottom layer of the OSI Model.
It is responsible for the actual physical connection between the devices. Such physical connection is made by using NICs, twisted-pair cables, and connectivity devices.
It is concerned with transmitting bits over a communication channel.

## Slide 28
Physical Layer (layer-1)
Functions provided by the Physical Layer:
Transforming bits into signals to be transmitted over the transmission medium
Provides synchronization of bits by a clock.
It defines the transmission media over the network.
It defines the transmission rate of the network.
It defines the way in which the devices are connected to the medium (physical topologies).

## Slide 29
The TCP/IP Model
Okay … by now you are familiar with the concept of the OSI model.
It’s time to understand how the real internet model is implemented.
That’s our next lesson: TCP/IP model

## Slide 30
Research Activity
The gateway is a connectivity device used in networking. Describe its function and identify at which layer it operates.
Explain what is meant by the “three-way handshake”. At which OSI layer does it take place?
** Explore the similarities and the differences between the OSI model and the TCP/IP model.